## Slide 1
State Road A1A/Ocean Blvd from
South of Grand Court to South of Linton Blvd
Financial Management Number: 444477-1-52-01
Public Workshop
March 13, 2023

## Slide 2: Meet the Team
Brad Salisbury, P.E.
Design Project Manager
FDOT
Walna Calixte
Community Outreach Specialist
Infinite Source Communications Group
Billy Scott, E.I.
Roadway Designer
FDOT
James Poole, P.E.
District Drainage Engineer
FDOT
Aaron Wilbur, PLA
Landscape Architect
Cotleur & Hearing

## Slide 3
Non-Discrimination Policy

## Slide 4
Project Location and Overview

## Slide 5: Project Limits: State Road A1A/Ocean Blvd from South of Grand Court to South of Linton Blvd
Spanish River
Blvd
End Project
Begin Project
Linton
Blvd
Meeting Location
Highland Beach Library Community Room

## Slide 6: Project Overview
  Proposed Improvements:
  Resurface roadway pavement
  Minor (2 ft - 3 ft) widening to accommodate bicycles on the roadway shoulders
  Extend Northbound Left Turn onto Linton Blvd
  Improve drainage in swales
  Upgrade signing and pavement markings to current standards
  Project Length: 3.4 miles
Notes:   Congestion relief by adding a third westbound left turn lane
  Mill and resurface the existing pavement
    Restore skid resistance
    Extend service life of the roadway
  Upgrade the following to current standards:
    Intersection lighting
    Curb ramps
    Signing & Pavement Markings

## Slide 7: Existing Conditions

## Slide 8: Proposed Improvements

## Slide 9: Drainage Swale Detail

## Slide 10: Temporary Traffic Control Plan
Work will be done in phases to reduce the impacts of construction in the community
Single lane closures will be done in segments
  No greater than 1,000 feet of lane closure during daytime hours
  No greater than 2,500 feet of lane closure during nighttime hours
Construction personnel will direct traffic during single lane closures to maintain two-way traffic
Pedestrian and vehicular access to all properties will be maintained at all times

## Slide 11: Project Schedule and Cost
  Estimated Construction Cost: $8.8 Million
August 2022
February 2022
60% Plans
April 2023
90% Plans
Public Meeting
August 2023
100% Plans
Spring 2024
CONSTRUCTION BEGINS
Summer 2025
PROJECT COMPLETE
March 2023
Public workshop

## Slide 12: Additional Comments/Questions
Please submit your comments by September 10, 2022
Attendees are able to submit comments and questions in writing form using a comment sheet.
All comments and questions are part of the Public Record.
If your question was not responded to during the event, a response will be provided later.

## Slide 13: Contact Information
If you have additional questions, please contact Brad Salisbury, P.E. –
FDOT Project Manager at:
Brad.Salisbury@dot.state.fl.us
3400 West Commercial Boulevard
Fort Lauderdale, Fl 33309
(954) 777-4160 or
Toll Free: (866) 336-8435; Ext. 4160

## Slide 14
Thank you!
For attending the Public Workshop